Timelapse camera

Raspberry Pi 5 has a ‘low power’ feature plus a Real Time Clock, which has a ‘wake up’ capability.

Seconds to wake up time can be inserted into a file which is read on going low power (Linux ‘shutdown’ but retaining power to the board). After the given seconds, the board powers up again.

This suggests a time lapse project:

I would like to take a mid-day photo of some apple trees throughout a year, to stitch in a film showing snow on bare trees, spring blossom, leafing up, growing apples, falling leaves.

Due to difficulty of getting power to the garden:

Solar panel plus battery with raspberry pi with camera, all boxed up and mounted.

Pi in low-power mode apart from brief mid-day on-time for the photo, plus an evening on-time to give myself a chance to connect and pull down photo’s or do any changes.

## Software

A Python script starts on boot and runs as a service.

Pi turns on for two periods each day which allows a photo to be taken at midday, and also allows a remote user to connect and turn off the service if required.

11:55 RTC powers up Pi
12:00 script takes photo, sets RTC wake up time to 18:00
        and turns power off

18:00 RTC powers up Pi
18:10 script sets RTC wake up time to 11:55 next day
        and turns power off

The script, continuously running:

Loop:

      If the hour is 12, and no photo taken yet, then take it

      If current time is between 12:00 and 17:55:
        Set RTC to turn Pi on at 18:00
        Shut down Pi

       If current time is between 18:10 and 11:50 next day:
        Set RTC to turn Pi on at 11:55
        Shut down Pi

       Otherwise, Wait 5 seconds, continue loop

## Power budget

Note: the 2GB version of the Pi5 has a tested current of less than 1A, assuming wattage of 5V x 1.0A

Assume on-time of 20 mins, energy used by Pi:

5V * 1A * 0.33h = 1.7 watt hours (Wh)

Assuming 0.05 Watt for standby during rest of day

0.05W * 24h = 1.2 Wh. (ignoring 20 mins less)

Total energy required for 24hr = 3.0 Wh

Waveshare power management unit, has 3x18650 Li-ion batteries providing 3x2500mAh,

Max battery energy capacity 5V x 7.5Ah = 37.5 Wh

So fully charged batteries have plenty of capacity.

Purchased two 6V 2.0W Solar panel, set in series (potentially 4W)

Assume UK weather only gets 1W, then after four hours of daylight:

  1.0(W) x 4(h) = 4 Wh

So should get the 3Wh energy required per 24hr.